## Slide 1: Automated detection and classification of events in the time series of hydraulic sensors
Alexander Mačejovský, Štěpán Pardubický

## Slide 2: Task
Assigned by DHI, a water management company
Automated detection and correction of errors
in time series of waste-water measurements
Constraints given by the client: no targets, univariate
Output: practically usable Python library

## Slide 3: Data
8 time series, each several moths long
Noisy, rain has large impact
Stepan

## Slide 4: Detection of events
Machine learning methods
Visual inspection and heurisitcal methods
Stepan

## Slide 5: Types of errors
Zero and constant values
Outliers and prolonged drops
Heightened volatility

## Slide 6: Zero and constant values
Straightforward, easy to identify

## Slide 7: Outliers
Large jump there and back again

## Slide 8: Prolonged drops
Measurements are hindered for some longer time
Stepan

## Slide 9: Heightened volatility
Suspiciously high volatility when compared to similar times of day on different days

## Slide 10: Heightened volatility
Identified by large moving standard deviation of the first differences

## Slide 11: Corrections
Depend on the length of sensor’s malfunction:
Short-term errors (<8 periods)
Medium-term errors (8-60 periods)
Long-term errors (>60 periods)

## Slide 12: Short-term corrections
Simple smoothing, practically enough
Stepan

## Slide 13: Medium-term corrections
Predictions from ARIMA models, by default ARIMA(3,1,2), based on 200 prior observations
Not fully implemented

## Slide 14: Long-term corrections
Take advantage of cyclicity
Not yet implemented
Stepan

## Slide 15: Python library
Graphical tools
Automated detection and corrections
Option for changing parameters for individual time series or even individual groups of errors

## Slide 16: Conclusion
Managed to create quite multi-functional library which can be easily used for automatized detection and partially also for correction of errors
Stepan

## Slide 17: Thank you for your attention!